## Slide 1: Module 5 Risk assessment and hazard avoidance
5.1.1 Preparations for on-site arrival, en-route (upwind) approach, incident analysis. On-site risk/threat assessment.
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Module 5 Risk assessment and hazard avoidance
Result: trainees know what part of the curriculum is presented and who is the targeted audience
Instructions for the trainer: Introduction slide of the module
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: learning objective
Result: trainees know what part of the curriculum is presented and who is the targeted audience
Instructions for the trainer: Introduction slide of the module
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: Risk assessment on scene and hazard avoidance
The following topics are discussed:
En route, approach and arrival
Reconnaissance
Situation report (SITREP)
Ensure a safe working environment
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Risk assessment on scene and hazard avoidance (topics discussed)
Result: After this slide the trainees know what information will be discussed in this module
Instructions for the trainer:
Explain that these four topics will be discussed, and a scenario will be used as an interactive example to put the lesson into practice.
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 4: En-route (1)
Think in scenarios, ask yourself questions, plan and act accordingly
Which scenario do you expect at the scene?
  What are the hazards? (CBRN-agents?, terrorists, other threats?)
  What is a safe route to approach the incident (upwind)
  Are there victims? (number and type of injuries?)
  Which other response services are en-route, or on scene?
What is the effect of your planned actions?
  Are they mitigating the risk of contamination?
  Are they mitigating the number of victims?
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: En-route (1)
Result: After this slide the trainees know what to take into consideration when en-route and approaching the incident scene
Instructions for the trainer: Explain that the bullet points can help them to prepare for an incident they are responding to. Ask the trainees what points they consider already.
A short movie which could be used to start a discussion with the trainees: https://www.youtube.com/watch?v=PA28biQ77A4
Mention that this is a training video, and not an actual incident!
Ask the trainees what they think is important to know when they are en-route to the incident.
Give examples of incidents and ask the trainees to come up with scenarios that can be expected given that particular incident.
Point out not only to prepare for the best-case or most likely scenario, but also think about worst-case scenarios.
The bullet points can be used to structure your thoughts and help to respond more quickly and safely to a changing scenario.
References for additional information: FIRST RESPONDERS Handbook – Hazardous Materials CBRNE. 2014 ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: MSB FIRST RESPONDERS Handbook – Hazardous Materials CBRNE. 2014 ISBN 978-91-7383-412-4

## Slide 5: En-route (2)
What are the consequences of your actions?
  Is the risk of contamination reduced?
  Are victims treated and evacuated?
  Do I enable or hinder other units in doing their jobs?
  Am I still safe enough?
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: En-route (2)
Result: After this slide the trainees know what to take into consideration when en-route and approaching the incident scene
Instructions for the trainer: Explain that the bullet points can help them to prepare for an incident they are responding to. Ask the trainees what points they perform already.
A short movie which could be used to start a discussion with the trainees: https://www.youtube.com/watch?v=PA28biQ77A4
Mention that this is a training video, and not an actual incident!
Ask the trainees what they think is important to know when they are en-route to the incident.
Give examples of incidents and ask the trainees to come up with scenarios that can be expected given that particular incident.
Point out not only to prepare for the best or most likely scenario, but also think about worst-case scenarios.
The bullet points can be used to structure your thoughts and helps responding quicker and safer to a changing scenario.
References for additional information: FIRST RESPONDERS Handbook – Hazardous Materials CBRNE. 2014 ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: MSB FIRST RESPONDERS Handbook – Hazardous Materials CBRNE. 2014 ISBN 978-91-7383-412-4

## Slide 6
Arrival at the incident
Approach and arrival
Approach and stay upwind, at least 50 meters from the incident.
  Consider alternatives if a distance >50 meters is not possible or necessary.
Ensure accessibility to the scene for other emergency units.
  Do not block access and exit roads.
  Initiate a traffic circulation plan.
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Arrival at the incident
Result: After this slide the trainees know how to arrive safely at an incident, and what to do immediately after arrival at the incident scene
Instructions for the trainer: Explain what should be done immediately after arrival at the scene, point out and explain:
Approach the incident from upwind and stay at least 50 m away
  approaching from upwind reduces your risk of exposure to gases/vapours released at the incident
Ensure the accessibility to the area surrounding the incident location for other FR-units
  Obviously, FR vehicles should not block roads for other first responders
  A layout for a circulation plan for ambulances should be established
  Public traffic may need to be diverted to keep out of the area for safety and to leave the area free for emergency services to arrive and leave
  Identify the best/safest place for emergency services to park their vehicles
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 7: First actions - 1 Reconnaissance (1)
Reconnaissance
Perform a reconnaissance but stay safe
When proper PPE is available: perform a (quick) risk assessment
  Assess victims: numbers and symptoms
  Assess environment: e.g. abnormal gaseous clouds, liquid spills, abnormal soil/water colouration
  Escalate when necessary to higher command, and alert specialists and equipment, etc.
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: First actions – 1 Reconnaissance (1)
Result: After this slide the trainees know what to do after arrival, and what actions should be performed first based on the availability of proper PPE.
Instructions for the trainer:
Explain and point out that thinking ahead increases the scope of actions that you (as a FR) can perform on arrival
Do I have the proper PPE to perform a reconnaissance & (quick) risk assessment?, if so then:
  Do an assessment of the victims and the environment
  Escalate when it is obvious you need assistance
If not, what are the possible actions I can still perform?, for instance:
  Seek information from key personnel in the vicinity of the incident (employees in the vicinity)
  Escalate quickly to obtain assistance of FR with proper PPE or more specialist units
  Coordinate the incident: keep the public at a safe distance, assist in the arrival of FR and specialist units.
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 8: First actions - 1 Reconnaissance (2)
When no proper PPE is available: escalate and keep your distance
  Seek information from key personnel involved (technical operators, local experts, etc.)
  Scale up when necessary to higher command, and alert specialists and equipment, etc.
  Keep your distance and assist in coordination (e.g. in the cold zone)
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: First actions – 1 Reconnaissance (2)
Result: After this slide the trainees know what to do after arrival, and what actions should be performed first based on the availability of proper PPE.
Instructions for the trainer:
Explain and point out that thinking ahead increases your scope of actions you (as a FR) can perform on arrival
Do I have the proper PPE to perform a reconnaissance & (quick) risk assessment?, if so then:
  Do an assessment of the victims and the environment
  Escalate when it is obvious you need assistance
If not, what are the possible actions I can still perform?, for instance:
  Seek information from key personnel in the vicinity of the incident (employees in the vicinity)
  Escalate quickly to obtain assistance of FR with proper PPE or more specialist units
  Coordinate the incident: keep the public at a safe distance, assist in the arrival of FR and specialist units.
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 9: First actions - 3 Situation report
Situation report (SITREP) based on reconnaissance, contains ideally:
Number of people that are in need of rescue or (urgent) medical help
Number of casualties and victims (and their status: type of injuries & symptoms)
Identity (and amount) of hazardous material released (signs and symbols)
Resources needed (equipment)
Expert support needed (people)
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: First actions – 3 Situation report
Result: After this slide the trainees know what to include in a situation report, after having performed a reconnaissance
Instructions for the trainer:
Explain the bullet points in the slide regarding what should be included in a situation report.
Note:
Although information on the identity and amount of hazardous material released is of vital importance, signs and symbols at the incident scene are probably the only means available to identify CBRN agents.
Consider alerting specialist units en-route already, when you are informed that it is highly likely you responding to an CBRN-incident,. Ask the trainees if they have considered that already during the first slide.
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 10: First actions - 4 Ensure safe working environment
Ensure a safe working environment for emergency services
At the incident scene, ensure that
Potential new risks or hazards are identified quickly
Required distances are enforced to avoid any risks
Define required PPE for every zone (cold, warm and hot zones)
Define need for resources (responders, experts and tools)
In case of a terrorist attack
  Remain vigilant for a secondary attack on emergency services
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: First actions 4 Ensure safe working environment
Result: After this slide the trainees know what type of information or actions are required for a follow-up after their first actions
Instructions for the trainer: Explain that to ensure follow-up actions runs smoothly, the bullet points above can be of vital importance.
Keep in mind that complex incidents will require a multi-agency approach.
Ensure multidisciplinary cooperation as soon as possible. This gives you time to deal with things that you are primarily responsible for.
The HOT, - WARM and COLD zone layout is explained later in another module.
Define PPE and decontamination requirements as soon as possible. It can be of vital importance for your own safety and others.
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 11: Exercise time
A scenario discussion
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Exercise time
Result: trainees practice the four steps program: 1 en route, approach and arrival, 2, Reconnaissance, 3 Situation report (SITREP), and 4 Ensure a safe working environment
Instructions for the trainer: Total estimated time 20 minutes
Explain that this exercise is preferably performed in a single group, or in smaller subgroups if a single group is considered too large.
The setting is a group of responders en route, and performing a number of first actions immediately after arrival on scene.
In this exercise the trainees are the group of responders.
Depending on the background of the trainees, the group of responders can be a police patrol vehicle, fire brigade vehicle, or an ambulance, or represent all first responder groups.
Exercise
A group of responders are en route to an incident.
  The trainees should think about possible scenario’s (slide 3) and the first actions they are going to perform (slide 4).
  trainees should receive (basic) information about the incident, for instance gained from the scenario in module 4.1
The responders arrive at the scene of the incident.
  At this step, the trainees should be given a handout of slide 10 (scenario), or shown the presentation.
  The trainees should be able to perform the steps described in slide 5, and should point out where to perform which actions.
The group has performed a reconnaissance and has to provide a situation report to higher command.
  The trainees should be able to perform steps described in slide 7.
Note:
Take about 5 minutes for step 1, 10 minutes for step 2, and 5 minutes for step 3. Exercise stops after 20 minutes.
When performed in small groups (3-4 people), you may run out of time when each group explains their action separately.
As an alternative, you can pick a single group to perform the exercise, and ask the rest of the trainees for additional steps when the group has completed the exercise.
References for additional information: -
Depicted illustration: a timeline of a table-top exercise involving a nuclear power plant
Picture source & IP: RIVM fileserver (R:\VLH\Data\Foto-archief-VLH\2012\2012-03-09 Workshop BORI)
Text source & IP:

## Slide 12
21°C
3 BFT
Smoke is rising from trailer tank
Driver is present but not responsive
Victims present, some unconscious
Bystanders are present
SCENARIO
School
Shops
Park
Parking
Garage
(5 levels, 800 Places)
50 metres
Incident
Wind direction
MELODY road
EDEN street
PRACTICE avenue
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: SCENARIO
Result: After this slide the trainees have performed their first actions on arrival
Instructions for the trainer: EXERCISE:
This is a single slide with information that can be used by the trainees to initiate their first actions upon arrival at an incident.
This slide should be provided to the groups in the exercise at step 2 of the exercise.
This scenario is a follow up of the scenario in 4.1, and information provided there can be used as well.
ACTION :
trainees should make a first Situation report (Sitrep). Discuss the outcome of the different Situation reports among the trainees.
Let the trainees preform an in-depth risk assessments based on the information and situation report. Discuss the outcome with the trainees.
ADR sign: flammable liquids (class 3)
UN number and hazard code for transport: UN 1203 Gasoline
Hazard code (top): 3 (=flammable), 33 (=highly flammable)
Identification number: 1203 (=Gasoline or petrol or motor spirit).
If preferred, other substances can be used as well.
References for additional information: -
Depicted illustration: Clip Art of a CBRN incident
Picture source & IP: Melody
Text source & IP:

## Slide 13: Take home message
Apply the following actions during the response:
Approach: choose a safe route and keep up wind in your back
Distance: Incident related, but enforce required distances to avoid risks
PPE : Define, organize and apply necessary Personal Protective
Equipment
SITREP: Information on victims, CBRN-agents and required experts
Consider: React to changing conditions
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Take home message
Result: After this slide the trainees are able to provide a short list of vital actions to perform when en-route and when they arrive at the incident
Instructions for the trainer:
Wrap up your presentation with this take home message. Point out potential scenario development when thinking ahead.
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 14
Thank you for your attention
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.1 Preparations for on-site arrival, en-route, approach, incident analysis. On-site risk/threat assessment.
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Thank you
Result: After this slide the trainees have performed their first actions on upon arrival
Instructions for the trainer: -
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP: MELODY consortium