## Slide 1: Module 5 Risk assessment on scene and hazard avoidance
5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Module 5: Risk assessment on scene and hazard avoidance
Result:
Instructions for the trainer:
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To recognize how to carry out basic decontamination procedures for people and domestic animals
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Presentation 5.5: Decontamination (of people, domestic animals) Result: After this slide the trainees know what part of the curriculum is discussed
Instructions for the trainer: This slide explains the content of the practical training in 5.6.P.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: Decontamination
The reduction of C, B, R&N agents from surfaces of living organisms, soil, water or objects.
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Decontamination
Result: After this slide trainees will know what is meant with ‘decontamination’
Instructions for the trainer:
Start with the definition of decontamination.
Decontamination = The reduction of C, B, R&N contamination from surfaces of living organisms or objects, soil or water. "Reduction" is used since a 100% removal of the contamination is not feasible in all cases
An example is ‘washing your hands with water and soap’. Both water and soap are used to wash away the contamination.
Sometimes the term decontamination agent is used:
Usually this refers to a powder or liquid that can be applied to the skin or any other surface.
It adsorbs or destroys the hazardous substance.
Decontamination is applied to all contaminated persons. It is applied to objects or areas that may threaten spreading hazard in the further course of action, or may have value in some sort of way: the location itself, people, cars, tools detectors, objects that might have forensic value etc.
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration: A decontamination procedure practiced in the Netherlands with a special device to distribute the decontamination fluid. A metal ring is used to spread the fluid. The picture shows an exercise with experts from RIVM and the National Forensic Institute (NFI).
Picture source & IP: RIVM
Text source & IP:

## Slide 4
Vehicles and objects
Buildings, cars, pieces of evidence (like anthrax letters), tools, used in the field (like guns), etc.
Persons with protective clothing
Fire fighters, CBRN experts
Persons without protective clothing
First responders, bystanders, victims, offenders, etc.
Animals
domestics (like cats and dogs), farm animals
Categories
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Categories
Result: trainees will recognize that there are different categories of ‘what or who can be decontaminated’.
Instructions for the trainer: Explain the following:
Basically, anything that can become contaminated, can be decontaminated (which is a fancy word for ‘cleaning’), however, not always to a full 100%
Objects like cars or buildings, could need decontamination. In most countries the military is equipped for this type of decontamination. Also, the fire department is often able to carry out this kind of decontamination, especially for vehicles.
Persons with protective clothing can be decontaminated in a similar way as vehicles or objects as they are protected against the decontamination agent. However, more reactive decontaminants are usually not used for this purpose. Instead, clothing is removed, and decontamination is carried out with soap and water.
People without protective clothing include first responders, civilians, witnesses, victims, perdomesticrators, etc. They are much more vulnerable than those with protective clothing.
Animals are a challenge since it is hard to explain to them the process, while cooperation with the decontamination process is one of the key factors to success.
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration:
Picture source & IP:
Far left: licensed by shutterstock, purchased by SCK-CEN
Middle left: RIVM
Middle right: licensed by shutterstock, purchased by SCK-CEN
Far right (cat): licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 5: Vehicles and objects
Waiting for a liquid to vaporize or a gas to be blown away may be sufficient in some situations.
WET DECON: Decontamination liquids like soap, hypochlorite, hydrogen peroxide, etc. can be used.
DRY DECON: Adsorbents can be used for dry contamination.
Be aware that damage could be caused by water or corrosive fluids (e.g. in electrical system)
Forensic evidence such as fingerprints and DNA could be destroyed.
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Vehicles and objects
Result: trainees will gain some knowledge of decontamination of vehicles and objects
Instructions for the trainer: Explain the slide.
Note that large amounts of wastewater must be managed, when decontaminating vehicles and objects.
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration: decontamination of a large vehicle
Picture source & IP: licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 6: People with protective clothing
WET DECON: Usually wet decontamination followed by removal of protective clothing
Decontamination liquid could contain soap, hypochlorite, hydrogen peroxide, etc.
Removal of the protective clothing is the last and very effective step in the procedure
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: People with protective clothing
Result: trainees will obtain some basic knowledge of decontamination of people wearing protective clothing
Instructions for the trainer: Explain the slide.
Note that a limiting factor while carrying out decontamination might be the available breathing air for the first responder.
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration: cleaning of a person in a gas tight suit
Picture source & IP: licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 7: People without protective clothing
Decontamination is needed in case of liquid (or solid ) contamination. Not for airborne contamination.
DRY DECON: Removal of clothing is the most effective decontamination method!
Dry decontamination methods also include cleaning contaminated area with adsorbing tissue, bandage, towels, etc.
WET DECON: Use water to wash away any residues. Decontamination liquids must be non harmful (water, soap, etc.)
Pay extra attention to damaged skin. Do not damage the skin by e.g. scrubbing.
Consider cutting hair.
Watch out for hypothermia of wet and unclothed people
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: People without protective clothing
Result: trainees will have gained some basic knowledge of effective decontamination of people without protective clothing
Instructions for the trainer:
Explain the slide.
Decontamination is useful after exposure to solids or liquids. This includes small particles that could be transported through aerosols. Decontamination after exposure to gases is not needed (as gases are not retained in clothing)
Stress that removal of clothing is the most effective dry decontamination method.
Removal of clothing should be carried in a manner that minimizes the risks that outside layers of clothing touches inside layers or bare skin. Cutting clothes like jumpers and T-shirt with prestige medical bandage scissors is a way to minimize this risk.
Hence, save removal of clothing requires assistance by helpers and a social safe environment preserving privacy, dignity, and respecting cultural beliefs. Dry decontamination is usually followed by a wet decontamination method, often by using water.
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration: decontamination of bystander by the fire brigade
Picture source & IP:
upper image: Maartje Kuperus | Fotografie & Tekst www.maartjekuperus.nl maartje@maartjekuperus.nl
lower image licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 8: People without protective clothing
Most suitable decontamination procedure depends on:
  type of agent (liquid/ solid)
  degree of contamination
  medical condition of victim
  number of victims to be decontaminated
Exposure of first responders handling contaminated victims is prevented by wearing gloves. Inhalation of solids or volatile liquids from victims is rare and symptoms are mild and reversible
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: People without protective clothing (2)
Result: trainees will have gained some basic knowledge of effective decontamination of people without protective clothing
Instructions for the trainer:
Explain the slide.
Most suitable decontamination procedure depends on the factors that are mentioned: for 1 partially contaminated patient it may be unnecessary to start a procedure and washing with tapwater may be sufficient
Secondary toxicity from direct contact is prevented by wearing gloves. Secondary toxicity from inhalation is rare and not a very serious threat. Illustrate this by noting that doctors who treated patients from the sarin attacks in Japan and who did not have adequate PPE experienced only mild symptoms afterwards.
References for additional information:
Depicted illustration: Tokyo sarin attack
Picture source & IP: licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 9: Animals
The same guidelines as for people without protective clothing apply to animals.
Decontamination of animals may be difficult as they do not cooperate easily
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Animals
Result: trainees will obtain some basic information about decontamination of animals
Instructions for the trainer:
Explain the slide.
Note that animals are difficult to decontaminate because they do not easily cooperate with decontamination procedures
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration: Cat
Picture source & IP: licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 10: Decontamination line
Locate event and hazard on a map
Plume dispersion modelling can deliver size of effected area and used to set a safe location for a decontamination line
Planning decontamination line
Exemplary setup of a decontamination line
Shower
Dressing
Prep tent
Wind
domesticty items /Underwear removal
Outer garment removal
Identification and marking
Detection
Contamination staging posts
Emergency corridor
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Decontamination line
Result: trainees are able to understand the principles of operating a decontamination line.
Instructions for the trainer:
At a CBRN scene, usually a decontamination area is set up:
Decontamination area = The area where the decontamination is carried out.
There is a clear border between inner and outer safety perimeter.
All victims, personnel and equipment leaving the warm zone have to undergo decontamination before entering the cold zone
Discuss that it is helpful to have access to a map showing the modeled effected area to set a safe environment for the decontamination line, also taking to account access and exits roads.
Discuss that a decontamination station is set up in such a way that contaminated people move upwind while going through the consecutive stages in the decontamination process.
The example decontamination line shows activities to be performed on the line. Also include in the discussion necessary safety issues.
This slide will be discussed in more detail in the practical training
References for additional information: -
Depicted illustration: Printout from MARPLOT, drawing of decontamination line diagram
Picture source & IP: MELODY creation using ALOHA, MARPLOT and CAMEO software https://www.epa.gov
Text source & IP:

## Slide 11: Decontamination of professionals vs public
Professionals
Uniform outfit, offer some protection (fire brigade)
Bound by discipline, obliged to follow
Clear agenda
Public
Driven by natural & rational reaction to flee from danger
Confused priorities
Diverse agendas
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Mind the differences
Result: trainee understand that there’s a difference between decontamination of professionals and random incident attendants.
Instructions for the trainer:
Discuss the difference between trained professionals and public.
Different types of victims and event may require different approaches.
(This slide will be discussed in more detail in the practical training.)
Background:
It is an important point to add that responders/professionals are decontaminated in a separate area as part of safely managing their operations.
It is to be expected that trained professionals comply to instructions and are more easily ushered than untrained personnel and public
The public can by 'driven by panic' but that does not have to be their primary reaction. There is lots of research on this topic of 'panic' - what it is and what it is not.... it is natural and rational to flee from danger and it is a predictable survival response.
The public usually comply and cooperate with emergency responders when they receive help and good communication about (de)contamination
e.g. "take off your outer clothing and we will bring help to you and decontaminate you"
When there is an inefficient response/no help/poor communication/delay waiting for decontamination, the public want to leave the danger area for their safety. In actual fact, the responders may be keeping them in danger of further contamination from each other or further terrorist attack.
Best practice is to promote the principles that need to be used to best understand, protect and influence the public reaction - how to use good communication and self help/reliance factors to gain cooperation.
Sometimes the emergency services blame the public for not doing what they wanted and the say it was 'panic', while afterwards evaluations showed that emergency services did not provide the right guidance and help at the scene, or the response was slow and uncoordinated so the public just had to do what they thought was best instead.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 12: Take home message
Set up clear and swift communications what will happen in the decontamination process
Victims should be decontaminated in the warm zone.
Removal of clothing then water and soap is usually very effective.
Any available adsorbent material can be used for decontamination: absorbent tissue, towels, wound dressings, etc. .
Hypochlorite is effective against many CBRN agents but is a harmful chemical and should only be used by experts.
Avoidance of (secondary) contamination: basic hygiene!
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Take home message.
Result: trainees take home message: some rules of thumb for decontamination.
Instructions for the trainer:
Discuss the listed Take home messages
References for additional information: https://chemm.nlm.nih.gov/decontamination.htm
Depicted illustration:
Picture source & IP:
Text source & IP:
Some text from: Project 54 Capacity building for medical preparedness and response to CBRN incidents Module 2, Session 2 Emergency Response to CBRN incidents – Overview

## Slide 13
Thank you for your attention
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Notes: Module 5 Risk assessment on scene and hazard avoidance
Learning objective: To recognize how to carry out basic decontamination procedures for people and domestic animals
Melody Presentation 5.5 Decontamination (of people and domestic animals)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Thank you for your attention
Result:
Instructions for the trainer:
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: