## Slide 1: Module 5 Risk assessment and hazard avoidance
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Module 5: Risk assessment and hazard avoidance
Result: trainees know what part of the curriculum is presented and who is the targeted audience
Instructions for the trainer: Introduction slide of the module
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: learning objective
Result: trainees know what part of the curriculum is presented and who is the targeted audience
Instructions for the trainer: Introduction slide of the module
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: Risk assessment on scene and hazard avoidance
The following topics are discussed:
Establish hot, warm, and cold zones.
Ask for, or notify, additional specialists on CBRNE.
Cordon off contaminated areas.
Evacuate contaminated victims/casualties from hot zone to warm zone.
Provide safe work conditions for first and secondary responders.
Carry out necessary rescues and first aid.
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Risk assessment on scene and hazard avoidance (Topic discussed)
Result: After this slide the trainees know what information will be discussed in this module
Instructions for the trainer:
Explain that these six topics will be discussed, and a scenario will be used as an interactive example to put the lesson into practice.
References for additional information: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 4: Follow-up actions (1)
Establish hot, warm, and cold zones
Define zones in consultation with multi disciplinary responders
Differentiate the danger zone in an inner (hot/warm) and outer zone (cold)
  Hot zone: only first responders, or specialists, with adequate PPE will be active.
  Warm zone: area with contaminated victims, clothes and materials.
  health risks can not be excluded, PPE may be required.
  Cold zone: a safe area, that has to remain safe. No PPE required
Fence off every zone with visible means and warn people in the vicinity.
  This may require extra personnel to warn or evacuate people.
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Follow-up actions (1)
Result: After these slides the trainees know the type of zones that are generally setup at an CBRN incident
Instructions for the trainer: Explain the three zones that are commonly used to differentiate between zones. Ask the trainees:
Which actions of the previous modules are performed in each of the zones? (approach & arrival, reconnaissance, sitrep, and ensuring a safe working environment for emergency services), walk through all the steps.
Note that in the European CBRN glossary only two zones are identified: an Inner safety perimeter (hot zone), and an Outer Safety Perimeter (cold zone)
Discuss with your trainees what other organizations you would like to have at this incident? And why? What should they bring along?
References for additional information: Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 5: Follow-up actions (2)
Hot zone
Rescue and evacuation only.
Life or health threatening exposure or contamination. PPE required
Warm zone
First aid and decontamination only
Contaminated area. PPE required
Cold zone
Safe area. No PPE required.
Staging area for first responders.
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Follow-up actions (2)
Result: After these slides the trainees know the type of zones that are generally setup at a CBRN incident
Instructions for the trainer:
Explain that weather conditions and wind direction can change during the incident. Be aware of this and take tactical measures to accommodate changing (weather) conditions. Communicate efficiently and try to minimize actions that can frustrate others.
Explain the three different zones:
HOT ZONE The hot zone is the area where the actual incident occurred and contamination exists. All individuals entering the hot zone must wear the prescribed levels of personal protective equipment and then be decontaminated correctly before leaving the hot zone. Check points will be established at the outer boundary of the hot zone to regulate the entry and exit of personnel and equipment. The outer boundary of the hot zone is initially established by visually surveying the immediate area and determining where the hazardous materials involved are located. Monitoring equipment may also be used to define the area.
WARM ZONE The warm zone is the transitional area between the hot zone and the cold zone. This zone generally contains the decontamination area and access control points through which personnel and equipment enter and exit. Since this zone is less hazardous, personnel can wear lower levels of personal protection equipment.
COLD ZONE The cold zone is the outermost part of the site and is considered non-contaminated. This is where the command post is located, along with support equipment. Normal work clothes are acceptable in this area. The command post should be situated upwind and upstream of the hot zone and should be easily accessible to highways or other transportation routes. The press is allowed in this zone.
The size and distances between the hot zone, warm zone, cold zone and the command post is based on conditions specific to each incident, the material involved, and the judgment of the incident commander.
Note that in the European CBRN glossary only two zones are identified: an Inner safety perimeter (hot zone), and an Outer Safety Perimeter (cold zone)
References for additional information: Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration: Schedule of the different zoning.
Picture source & IP: EU PROJECT 54 TRAINING COURSE HANDBOOK – CBRNE Standard Operating Procedures (2019)
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 6: Follow-up actions (3)
Ask for, or notify, additional specialists on CBRNE (if not done yet)
Cordon off contaminated areas. Only first responders with proper PPE are allowed.
Evacuate contaminated victims/casualties from the hot zone into a quarantine (holding) area in the warm zone.
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Follow-up actions (3)
Result: After this slide the trainees know the normal steps to take after zoning
Instructions for the trainer: walk through the steps.
As a first responder:
Always be aware of what you need to deal with the incident and ask for additional specialists in the case of CBRN (people, other agencies, technical advice and/or equipment).
Cordon off the contaminated areas. Only allow responders that wear the proper PPE.
Establish a quarantine (holding) area for contaminated victims and casualties. If people can walk, hold them in the warm zone.
Emphasize that zoning is important for both the general public and first responders.
There may be other hazards present as well, besides CBRN. For instance: collapsing structures, explosions, fire, etc.
Discuss with your trainees what other organizations you would like to have at this incident? And why? What should they bring along?
References for additional information: Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4
Depicted illustration:
Picture source & IP:
Text source & IP: “Handbook for FIRST RESPONDERS, Hazardous Materials – CBRNE”. DSB/MSB (2014) ISBN 978-91-7383-412-4

## Slide 7: Follow-up actions (4)
Provide safe work conditions for first and secondary responders
Carry out necessary rescues and first aid
  Remain vigilant for secondary contamination victim=>responder
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Follow-up actions (4)
Result: After this slide the trainees know the normal steps to take after zoning
Instructions for the trainer: walk through the steps.
After the zoning is established, if possible, organize two different decontamination areas. One for the public emergency, with large scale capabilities; the second one for the first responders and their equipment.
Accompany casualties to the decontamination units, after which medical help can be applied. Realize that this can only be done when having proper PPE.
Consider all requirements and provide transport for victims or casualties.
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP: Project 44 WP4 Train-the-trainers and training activities on CBRN incident response for the countries in the Black Sea region. Presentation T2/7 Zoning of incident area,scene management

## Slide 8: Exercise time
A short table top exercise
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Exercise time
Result: trainees practice the steps involved to implement the zones and take follow-up actions
Instructions for the trainer: Total estimated time 20 minutes
Explain that this exercise is preferably performed in a single group, or larger groups. For instance, a combination of first responders attending the scene.
The setting is a group of responders on scene, which have just performed their first actions immediately after arrival on scene.
Exercise
The group has to set up hot, warm, and cold zones after their first actions immediately after arrival on scene
  trainees should have the information gained from the scenario in module 5.3 and given a handout of slide 9
  The trainees should be able to setup hot, warm, and cold zones according slides 4 and 5.
  They can draw the zones accordingly on the handout.
After the three zones are set up, the trainees should perform a number of follow-up actions
  The trainees should be able to perform the steps described in slide 6 and 7
  The trainees should point out where to perform the specific actions on the handout
Note:
Take about 10 minutes for step 1, and 10 minutes for step 2. Exercise stops after 20 minutes.
When performed in small groups (3-4 people), you may run out of time when each group explains their action separately.
As an alternative, you can pick a single group to perform the exercise and ask the rest of the trainees for additional steps when the group has completed the exercise.
References for additional information: -
Depicted illustration: a time line of a table-top exercise involving a nuclear power plant
Picture source & IP: RIVM fileserver (R:\VLH\Data\Foto-archief-VLH\2012\2012-03-09 Workshop BORI)
Text source & IP:

## Slide 9
Smoke is rising from trailer tank
Driver is present but not responsive
Victims present, some unconscious
Bystanders are present
SCENARIO
21°C
3 BFT
School
Shops
Park
Parking
Garage
(5 levels, 800 Places)
50 metres
Incident
Wind direction
MELODY road
EDEN street
PRACTICE avenue
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: SCENARIO
Result: After this slide the trainees have implemented zoning
Instructions for the trainer: EXERCISE: this is the first slide of two with information about the incident that can be used by the trainees to initiate their follow-up actions.
The group should be able to follow the six steps in this module and perform the follow-up actions using the information on this slide.
Note:
This first slide is an overview of the incident scene and can be used to establish the three zones: cold, warm and hot zones.
The group can draw the zones on a handout of this slide
The follow up actions that are performed can be pinpointed on the locations of the slide by the trainees
For guidance as to how large each zone should be with this specific hazard (gasoline/petrol UN number 1203), which according to the practitioner’s handbook issued by the Swedish Civil Contingencies Agency requires an initial safety distance of at least 100 m.
References for additional information: -
Depicted illustration: Clip Art showing an overview of an accident with a tank truck
Picture source & IP:
Melody
Elements:
https://depositphotos.com/148094647/stock-illustration-realistic-cars-and-trucks-police.html
Tank Truck: https://www.shutterstock.com/image-vector/truck-trailer-template-vector-isolated-car-471356600, licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 10
Smoke is rising from trailer tank
Driver is present but not responsive
Victims present, some unconscious
Bystanders are present
SCENARIO
21°C
3 BFT
School
Shops
Park
Parking
Garage
(5 levels, 800 Places)
50 metres
Incident
Wind direction
MELODY road
EDEN street
PRACTICE avenue
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: SCENARIO
Result: After this slide the trainees have implemented zoning
Instructions for the trainer: EXERCISE: this is the second slide of two with information of the zones that can be established.
Note:
This second slide is again an overview of the incident scene and can be used by the trainer to show how the three zones, cold, warm and hot zones can be/ should have been established.
The follow up actions can be named following the six steps using the information in the slide
The actions that are (and should be) performed can be explained and pinpointed on the locations of the slide by the trainer
For guidance as to how large each zone should be with this specific hazard (gasoline/petrol UN number 1203), which according to the practitioner’s handbook issued by the Swedish Civil Contingencies Agency requires an initial safety distance of at least 100 m.
References for additional information:
Depicted illustration: Clip Art showing an overview of an accident with a tank truck
Picture source & IP:
Melody
Elements:
https://depositphotos.com/148094647/stock-illustration-realistic-cars-and-trucks-police.html
Tank Truck: https://www.shutterstock.com/image-vector/truck-trailer-template-vector-isolated-car-471356600, licensed by shutterstock, purchased by SCK-CEN
Text source & IP:

## Slide 11: Take Home message
Cordon off contaminated areas for first responders and people (hot, warm and cold zone)
Evacuate contaminated victims from hot zone to warm zone for quarantine
Ask for, or notify, additional specialists on CBRN
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Take home message
Result: After this slide the trainees can summarize the actions they have to take or organize follow up actions after the first actions are completed
Instructions for the trainer: walk through the steps.
After the zoning is established, if possible, organize two different decontamination areas. One for the public emergency, with large scale capabilities; the second one for the first responders and their equipment.
Accompany casualties to the decontamination units, after which medical help can be applied. Realize that this can only be done when having proper PPE.
Consider all requirements and provide transport for victims or casualties.
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP: Project 44 WP4 Train-the-trainers and training activities on CBRN incident response for the countries in the Black Sea region. Presentation T2/7 Zoning of incident area, scene management

## Slide 12
Thank you for your attention
5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Notes: Module: 5 Risk assessment and hazard avoidance
Learning objective: To recognize how to carry out an on-site risk assessment, zoning of the area, and isolation and registration of victims
Melody Presentation: 5.1.2 Security of the area, upwind approach (including traffic control), hot zone, warm zone, cold zone
Target audience: Fire Brigade, Police, Ambulance Services
Title slide: Thank you for your attention
Result: After this slide the trainees have performed their first actions on arrival
Instructions for the trainer: -
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP: MELODY consortium