## Slide 1: Module 2 CBRN basics
2.3.2 Dangerous goods and UN codes
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: Module 2 CBRN basics
Result: Introduction to MELODY curriculum
Instructions for the trainer: Starting slide
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: learning objective
Result: Introduction to MELODY curriculum
Instructions for the trainer: Starting slide
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: CBRN Signs transport & storage
What type of load does this truck carry?
  How do you know this?
  Is there a CBRN risk?
?
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: CBRN Signs transport & storage
Result: After this part of the curriculum trainees have an idea where to look for information about Dangerous goods that are transported by road.
Instructions for the trainer:
Ask trainees if they know what kind of dangerous goods this truck might carry.
What signs do they see?
Interactive discussion with trainees about signs and triggers for CBRN material.
References for additional information:
Depicted illustration: Truck with several signs.
Picture source & IP: https://de.wikipedia.org/wiki/Datei:Tankauflieger_mit_ADR_Tafel_und_Zettel.jpg, (Unknown Author) Creative Commons
Text source & IP:

## Slide 4: ADR pictograms for transport
Symbol
Number
ADR:
European Agreement concerning the International Carriage of Dangerous Goods (including C, B and R/N) by Road.
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: ADR pictograms for transport
Result: After this part of the curriculum trainees can recognize signs for CBRN materials, according to ADR, and are able to interpret the most important signs.
Instructions for the trainer:
ADR originates from a French term (you do not need to know what it stands for) and refers to transporting hazardous material.
It is important to recognize the meaning of the symbols or at least get a feeling for the type of risk.
First focus on the ADR pictograms. Name them one by one (starting with 1 explosives, etc. up to 9 Miscellaneous.
Which ones are most relevant for the topic of CBRN?
Note: especially 2.3, 6.1, 6.2 and 7 are substances which could be referred to as CBRN agents. However, all signs point out a potential hazardous situation.
Ask the trainees the question ‘what does miscellaneous (nr 9) mean’ OR just explain that miscellaneous could pretty much include everything including: ‘unknown’.
Notice there are systems for transport by water and air as well. The symbols used remain the same.
References for additional information:
Depicted illustration: ADR signs for various hazardous materials, including potential C or RN materials. UN code sign (orange sign)
Picture source & IP: All ADR images are obtained from Wikipedia under creative common licenses: (Unknown Author) licensed under CC BY-SA
Text source & IP:

## Slide 5: UN number and hazard code for transport
Hazard code (top):
  Number indicates hazardous properties of substance.
  Example: 3 means flammable, 33 means very flammable.
UN number (bottom):
  United Nations numbers has four digits that identify hazardous materials, and articles.
  Kind of an ID for hazardous material. Example: 1203 means Gasoline or petrol or motor spirit.
Hazard code
UN number
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: UN number and hazard code for transport
Result: After this part of the curriculum trainees can recognize signs for CBRN materials, according to UN hazard codes and numbers.
Instructions for the trainer:
The UN uses orange signs as an indication for hazardous material during transport.
The upper number indicates the kind of material (e.g. a 3 is a flammable liquid and two 3’s is a very flammable liquid) and the lower number identifies the material to substance level.
Notice that the classes are similar to the ADR classes.
Specialist (in most countries from the fire department) will be able to immediately identify the hazardous material indicated by the sign. However, you do not have to know these codes by heart.
But know it is important to write these numbers down and report them to specialists and dispatch officer. Or take photos of the sign and send them to specialists.
References for additional information:
Depicted illustration: ADR signs for various hazardous materials, including potential C or RN materials. UN code sign (orange sign)
Picture source & IP: 1200px-ADR33_UN1203.svg.png (1200×900) (wikimedia.org) Wikipedia under creative common licenses: (Unknown Author) licensed under CC BY-SA
Text source & IP:

## Slide 6: GHS symbols for storage
GHS symbols:
Globally Harmonized System of Classification and Labelling of Chemicals.
.
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: GHS pictograms for storage
Result: After this part of the curriculum trainees can recognize signs for CBRN materials, according to GHS storage classification, and are able to interpret the most important signs.
Instructions for the trainer:
These symbols are for storage.
Slightly different and yet similar to the ADR symbols.
Notice that the GHS (Globally Harmonized System ) symbols don’t include B or R/N symbols.
References for additional information: https://en.wikipedia.org/wiki/GHS_hazard_pictograms
Depicted illustration: image of pictograms indicating of hazardous materials for storage.
Picture source & IP: All GHS symbol images are obtained from Wikipedia under creative common licenses: (Unknown Author) licensed under CC BY-SA
Text source & IP:

## Slide 7: Biohazard sign
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: Examples biohazard sign
Result: The student can recognize the general sign for a biological hazard and understands the context.
Instructions for the trainer:
On the left picture you see the symbol for biohazard.
The right picture is a container for the safe disposal of sharps (e.g. needles) possibly containing biological hazardous material (e.g. blood with infectious disease).
References for additional information:
Depicted illustration:
Left Biohazard symbol
Right: immediate disposal of used needles into a sharps container is standard procedure.
Picture source & IP:
https://en.wikipedia.org/wiki/Biological_hazard#/media/File:Biohazard_symbol_(black_and_yellow).png, creative commons: public domain
https://en.wikipedia.org/wiki/Biological_hazard#/media/File:Sharps_Container.jpg, creative commons: CC BY 2.5 (no changes)
Text source & IP:

## Slide 8: Radiological sign
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: Radiological sign
Result: The student can recognize signs for Radiological and Nuclear materials and understands the context.
Instructions for the trainer:
As you can see at the picture on the left, a train is transporting radioactive material. Notice that the symbol (black symbol on yellow background) indicating radioactive material is visible on the side of the train.
The right picture is of a nuclear waste facility storing low-level waste barrels. Notice that transport containing high levels of nuclear materials usually is done by train (and in some countries that attracts protests).
Notice that the storage of nuclear waste is for the long term.
Notice the symbol (in red colour) for radioactivity on the yellow barrels. The shape of the symbol determines the presence of radiation, not the color of the symbol.
References for additional information:
Depicted illustration:
Left picture Spent fuel flasks transported by railway in the United Kingdom.
Right picture Storage of radioactive waste
Picture source & IP:
File: https://en.wikipedia.org/wiki/Radioactive_waste#/media/File:Nuclear_waste_flask_train_at_Bristol_Temple_Meads_02.jpg CC BY-SA 4.0
File: TINT Radioactive wastes' barrel.jpghttps://en.wikipedia.org/wiki/Radioactive_waste CC BY-SA 4.0
Text source & IP:

## Slide 9: Disclaimer
Criminals do not always label hazardous materials correctly.
Not all countries worldwide use the ADR and UN system for hazardous material.
Labels can get lost, damaged, etc.
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: Disclaimer
Result: The student realizes signs and symbols are not (properly) used at all times.
Instructions for the trainer:
The trainees have learned there are different signs and symbols to be used for the identification of hazardous material.
However, signs and symbols are not always properly used. Examples for improper use:
  Criminals are not in the habit of labeling hazardous materials. Sometimes (examples known in the Netherlands in relation to synthesis of drugs) even mis-informative symbols might be used to cover up illegal activities.
  Not all countries in the world are United Nations Member States (and therefor probably will not use UN codes for hazardous materials) nor do all countries make use of ADR or GHS symbols. Therefore, hazardous materials handled in non-EU countries might be labeled differently or not labeled at all.
  Labels or packaging material might get damaged or get lost.
References for additional information:
Depicted illustration:
Left: Images of the TV series Criminal Minds.
Reight: a map of the world indicating UN members.
Picture source & IP:
Left: https://en.wikipedia.org/wiki/Criminal_Minds#/media/File:Criminal-Minds.svg | public domain
Right: https://en.wikipedia.org/wiki/Sovereign_state#/media/File:United_Nations_Members.svg | CC BY-SA 3.0 (no changes)
Text source & IP:

## Slide 10: A short test:
Do you recall the meaning of the following symbols?
A
C
B
E
G
F
H
D
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: Do you recall the meaning of the following symbols?
Result: After this part of the curriculum trainees can recognize signs for CBRN materials and interpret the most important signs.
Instructions for the trainer: If you know these symbols this might help you in the field. Do you know them by heart?
A = radiological
B=flammable
C=danger to environment
D=cylinder
E=biohazard
F=Explosive
G=corrosive
H=toxic.
References for additional information:
Depicted illustration: Various symbols of pictograms indicating CBRN materials
Picture source & IP: images from Wikipedia, all in public domain
Text source & IP:

## Slide 11: Take home message
CBRN agents and materials can be recognized by various signs and symbols:
  ADR pictograms for transport
  UN number and hazard code for transport
  GHS symbols for storage
perpetrators will not likely pay attention to correct labelling of hazardous materials
Although used across the globe, not all countries use the ADR and UN system for hazardous material
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: Take home message
Result: The trainees are made aware of the differences and overlap in signs for CBRN agents in general, transport, and storage.
Instructions for the trainer:
The take home message is that CBRN agents can be recognized by various signs and symbols, used in Transport and Storage. These pictograms are used across the globe, but some nations do not use them. In addition, people with criminal intent will not use these symbols and signs for obvious reasons.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 12
Thank you for your attention
MELODY Presentation 2.3.2: Dangerous goods and UN codes
Notes: Module: 2 CBRN Basics
Learning objective: To recognize potential sources of CBRN agents, signs of dangerous goods, and improvised production facilities
MELODY presentation: 2.3.2 Dangerous goods and UN codes
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services
Title slide: thank you for your attention
Result: trainees and trainer wrap up this part of the curriculum and can move to the next topic.
Instructions for the trainer: Time for questions or remarks.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: