## Slide 1: Module 5: Risk assessment on scene and hazard avoidance
5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Module 5: Risk assessment on scene and hazard avoidance
Result: Student are made aware of the contents of this MELODY module
Instructions for the teacher: Note that in this MELODY module various types of Personal Protective Equipment (PPE) will be explained.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To recognize some different types of PPE and recognize how to carry out some basic techniques
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: learning objective
Result: Student are made aware of the contents of this MELODY module
Instructions for the teacher: Note that in this MELODY module various types of Personal Protective Equipment (PPE) will be explained.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: Personal Protective Equipment I (PPE)
PPE is essential for first responder personnel in the event of a CBRN incident.
PPE availability often differs between first responder groups, responding to the same incident
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Personal Protective Equipment I (PPE)
Result: After this slide the target audience will be aware a normal uniform has limited protective properties and additional PPE might be necessary
Instructions for the teacher:
In general the availability of PPE differs amongst groups of first responder. This is mainly caused by the different tasks these first responder groups have at an incident site. For example:
  Police officers might have clothing, gloves and masks for handling wounded persons or to conduct a forensic investigation;
  Fire fighters usually have protective clothing and independent breathing apparatus for protection against heat, smoke or dangerous chemicals;
  Ambulance personnel usually have protective clothing, gloves and masks for protection against body fluids and infectious diseases.
A dispatch officer should be aware that incident information might help the first responder to choose the right PPE
First responders must know the PPE available to them and should have an understanding of their possibilities and limitations.
In the event of a CBRN incident, additional PPE might be required, which often means escalating to the next level of expertise. It helps if the student has an understanding of PPE that other first responders or specialists may have.
References for additional information: -
‘EU PROJECT 54 TRAINING COURSE HANDBOOK (in English) CBRNE Standard Operating Procedures‘
https://chemm.nlm.nih.gov/ppe.htm
http://www.population-protection.eu/prilohy/casopis/eng/21/101.pdf
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 4: Personal Protective Equipment II (PPE)
‘Simple protective measures’ will be available for most first responders.
However, the level of protection has limitations.
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Personal Protective Equipment II (PPE)
Result: After this slide students have a first impression of what PPE means
Instructions for the teacher:
Possibilities for personal protective measures for CBRN incidents will differ greatly among different first responders, countries, etc.
In general fire fighters will have the best protective clothing, followed by ambulance personnel, followed by police officers.
However, all will usually have some form of protective clothing, e.g. disposable gloves and coveralls for dermal protection, and face masks for respiratory protection.
With regard to their own safety, if PPE is limited for first responders, an assessment of their tasks on scene (and potential reassignment) should be part of the risk assessment when arriving.
References for additional information: -
‘EU PROJECT 54 TRAINING COURSE HANDBOOK (in English) CBRNE Standard Operating Procedures‘
https://chemm.nlm.nih.gov/ppe.htm
http://www.population-protection.eu/prilohy/casopis/eng/21/101.pdf
https://www.cdc.gov/niosh/docs/2008-132/default.html
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 5: Personal Protective Equipment III (PPE)
Selection of PPE against CBRN agents when arriving on scene, can be based on:
Environmental indicators
Symptoms of victims
Choking &
heaving
Cramps &
vomiting
Burns &
blisters
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Personal Protective Equipment III (PPE)
Result: After this slide the choice of proper PPE is related to either symptoms of victims or environmental indicators.
Instructions for the teacher: Choosing PPE can be based on:
Incident information. The incident scenario is CBRN related.
Symptoms of victims on scene.
Environmental information available (e.g. signs of contamination).
Any other sign, symbols or triggers.
Basically, respiratory PPE blocks exposure by inhalation and ingestion, and dermal PPE blocks exposure by direct contact (skin).
References for additional information:
Depicted illustration:
Left: Environmental contamination of a stream,
Right: Clip Art of people showing symptoms: Choking & heaving, Cramps & vomiting, Burns & blisters
Picture source & IP:
Environmental contamination: RIVM
Symptoms: Noun Project Search, https://thenounproject.com/thenounproject.com
Text source & IP: RIVM

## Slide 6: Respiratory Protective Equipment I
Breathing apparatus (BA)
  supply of breathing-quality air from an independent source (cylinders)
  Time is limited, but could be extended by using a hose with an external air source
Respirator (filtering device)
  Different types of filters available (protecting from different types of gases)
  Filter masks can be powered or unpowered
  decreasing level of protection
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Respiratory Protective Equipment I
Result: After this slide the students know the difference between an independent breathing apparatus and a filter mask.
Instructions for the teacher:
Explain that the images shown are two examples of respiratory PPE often used by first responders
The top image shows breathing equipment, supplied by independent air sources, used by fire fighters and sometimes specialized police forces. The cylinder tank contains high pressured air (usually up to 300 bar). The pressure is reduced to a little bit more than the normal air pressure in the breathing mask. This means an overpressure of air in the mask will prevent inhalation of external gas. This type of PPE protects from all hazardous gases (since you bring your own bottle of air). However, working time is limited (usually somewhere between 30 minutes and 60 minutes, depending on the amount of air needed – e.g. heavy labor leads to the consumption of additional air).
The lower picture shows a full mask respirator filtering devices. These devices use disposable filter sets to filter air. There are different types of filters used for different types of hazardous gases. This means you should have an indication of what type of gas is present, though there also are filters designed for a combination of different groups of gases. However, for some gases this type of filter is not effective; one toxic gas that is not filtered effectively is carbon monoxide (CO).
Explain that the images show PPE with decreasing protection from top to bottom
References for additional information: -
Depicted illustration: Self-contained breathing apparatus and a respirator mask
Picture source & IP: Breathing apparatus and respirator
"A nice night for a Breathing Apparatus Support exam." by apples62 is licensed under CC BY-NC-ND 2.0
"respirator 002" by ChuckHolton is licensed under CC BY-NC-SA 2.0
Text source & IP:

## Slide 7: Respiratory Protective Equipment II
Respiratory protective masks
  FFP3 (95-98% effective)
  FFP2 (89-92% effective)
  FFP1 (75-78% effective)
Surgical masks (≠ respiratory protective gear)
  decreasing level of protection
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Respiratory Protective Equipment II
Result: After this slide the students know the difference between a respiratory protective mask and a surgical mask.
Instructions for the teacher: Explain that the images shown are two other examples of respiratory PPE often used by first responders.
The upper picture shows a FFP masks (FFP: Filtering FacePiece Particals). There are different types of FFP masks with different levels of protection (FFP3 being the most effective). For FFP masks, fitting tests are required to be effective in their specific range (FFP1-FFP3). These types of masks will protect against very small particles (such as viruses), but will give no protection against gases.
The bottom picture shows a relatively ill fitting surgical mask, which provides limited respiratory protection. It will give some protection against droplets (as created by coughing and sneezing saliva of the patient or doctor). However, no protection against gases is given.
References for additional information:
Depicted illustration: Respiratory face masks
Picture source & IP:
"Hand hält eine Aura FFP3 Atemschutzmaske 9332+ von 3M vor weißem Hintergrund" by verchmarco is licensed under CC BY 2.0
"Surgical face mask.jpg" by NurseTogether is licensed under CC BY-SA 4.0
Text source & IP:

## Slide 8: Respiratory Protective Equipment III
To ensure optimal protection from wearing a mask , pay attention to:
  Have a quality control regime in place for PPE that includes:
    Expiration time of the mask
    Fit tests to ensure proper fit
  A shaven face gives the best fit. A beard will cause leakage of the mask.
  Before entering the incident area
    Ensure PPE is properly donned
    Perform buddy checks to ensure proper fit
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Respiratory Protective Equipment III
Result: After this slide the student has learned some tips on effectiveness of masks
Instructions for the teacher: Explain that some factors may have a negative impact on the effectiveness of masks.
Masks may have an expiration date and a maximum time of use. For example, filter masks that filter gases contain some sort of absorbent (e.g. active carbon) to neutralize hazardous gases. The absorbent capacity will be limited and therefore at some point, hazardous gases may get trough the filter. The manual of the filter bus will provide detailed information about this subject.
People have different shaped heads, and one mask may fit better than others.
Facial hair (particularly beards) may have a big influence on its effectiveness. Some first responders therefore always shave when on duty.
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 9: Dermal Protective Equipment (suits)
Gastight suits (Level A)
  Gastight
  Chemical resistant
  Independent air supply
Chemical resistant suits (Level B)
  Chemical resistant
  (In)dependent air supply
Coveralls & aprons (Level C)
  Body fluid/dust resistant
  Full face respirators
Melody Presentation 5.4. Personal protective Equipment (PPE)
Level A Level B Level C
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Dermal Protective Equipment (PPE)
Result: After this slide the student has an idea of different types of protective suits.
Instructions for the teacher:
Explain that the images shown are examples of dermal PPE, which always has to be used in combination with respiratory PPE.
The examples shown are often not available for first responders, but are used by specialists.
The left image shows the best dermal and respiratory PPE available: a gas tight suit accompanied by independent breathing equipment with an independent air source. Notice that the breathing apparatus is worn inside the suit and that the suit is an overpressure environment. This type of suit is often used by specialists of the fire department. Time inside the suit is limited due to heat stress and the amount of air in the cylinder.
The middle image shows a chemical-resistant suit, accompanied by independent breathing equipment as well. Notice that the breathing apparatus is worn over the suit, so there is NO overpressure inside the suit. This means a person wearing this suit occupies less space compared to when wearing a gastight suit and therefore has more flexibility in the field. Often, the suit is less resistant to chemicals than the gastight suit.
The right picture shows a non-chemical resistant coverall as dermal PPE, accompanied by a FFP dust mask as respiratory PPE.
Level A is best protected and level C the least.
Notice that all levels (A-C) use gloves and some sort of safety boots. Also, good to notice: no matter how resistant the suit is to chemicals, at some point (after a long time of exposure or extremely high concentrations of chemicals) resistance will decrease. The protective effect will vary between chemicals.
References for additional information:
Depicted illustration: various levels of protective equipment
Picture source & IP: © Don Bodat – Photography, Creative Common License CC BY-ND
Text source & IP:

## Slide 10: Dermal Protective Equipment (gloves I)
Gloves are made of a variety of materials
  For example: latex, nitrile, etc.
  Materials used determine the protective properties
Different symbols indicate protective properties
  For example: protective against fire, mechanical damage, etc.
  Within these categories different types may be available with different properties
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Dermal Protective Equipment (gloves I)
Result: After this slide the students have an idea of different types of gloves and symbols indicating their properties.
Instructions for the teacher: Gloves are produced for different purposes. They vary in the type of material they are made of and their thickness, which affects their protective properties, but also their ease of use. Different materials will protect against different chemical substances.
The symbols depicted indicate:
Sign of European Norm EN 407: Protective gloves against thermal risks (Heat and/or fire)
Sign of European Norm EN 388: Protective gloves against mechanical risks
References for additional information:
Depicted illustration:
Protective gloves against thermal risks (Sign of European Norm EN 407)
Protective gloves against mechanical risks (Sign of European Norm EN 388 )
Picture source & IP:
https://commons.wikimedia.org/wiki/File:EN407pictogram2.jpg
https://commons.wikimedia.org/wiki/File:EN_388_sign.jpg
Text source & IP:

## Slide 11: Dermal Protective Equipment (gloves II)
For CBRN the following categories are relevant
Chemical risk compliant:
  Symbol of Erlenmeyer flask with liquid and vapor
  Additional numbers, letters, types for specific (group) of chemicals
Biological risk compliant:
  Biohazard symbol
  Different types of gloves are available
Radiation risk compliant:
  Symbol of electrons indicating protection against contamination
  radiation symbol for gloves with limited protection against radiation
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Dermal Protective Equipment (gloves II)
Result: First responders are made aware they should look for symbols on the glove or packaging material to get an idea of their protective properties.
Instructions for the teacher: Go through the 3 different categories: chemical, biological, radiological. Explain that within these categories different types may be available. For instance, there are chemical gloves for all kinds of chemicals, so whether or not a glove provides protection depends on the chemical it is exposed to. The instruction/manual of the gloves should provide this essential information.
References for additional information:
Depicted illustration: Protective gloves Signs
Picture source & IP: https://www.2mains.ch/en/course/full/2
The Melody consortium has done its utmost to trace the copyright owner of the photo used in the current presentation under fair use conditions. In case your photo hasn’t been properly acknowledged, please contact www.melodytraining.eu and the photo will be removed.
Text source & IP:

## Slide 12: Dermal Protective Equipment (gloves III)
Most gloves will have a combination of protective properties, of which a number are shown in the images below as an example
As you can see this example has a combination of protective properties.
PPE effective against chemicals will usually be effective against biological material and give some (but limited) protection in case of radioactive materials
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Dermal Protective Equipment (gloves II)
Result: Students learn that gloves can provide protection against a combination of threats.
Instructions for the teacher:
Example of a number of properties of gloves, indicated by various signs As you can see different signs are shown; not all details of the symbols (letters, numbers) are explained in this course. Notice this glove will protect against multiple threats.
Also note that (in general) some properties provide more protection, but are also less flexible and therefore limit movement of the hand and fingers. Therefore, a surgeon needs a very thin glove which gives freedom for finger movement while a gardener may use less flexible gloves.
References for additional information:
Depicted illustration:
Picture source & IP:
https://www.2mains.ch/en/course/2/slide/15
https://armoursafety.co.nz/products/Hand-Protection/DGBLHR
The Melody consortium has done its utmost to trace the copyright owner of the photo used in the current presentation under fair use conditions. In case your photo hasn’t been properly acknowledged, please contact www.melodytraining.eu and the photo will be removed.
Text source & IP:

## Slide 13: Other types of PPE
Safety goggles or screen caps
  Protection against splashes
Safety boots and shoes
  Protection against spills
Boot/shoe covers
  To prevent dissemination
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Other types of PPE
Result: Students learn about some additional PPE protecting eyes and feet.
Instructions for the teacher: Go through the items shown on this slide providing protection for the eyes and feet. Safety boots protect the wearer and shoe covers protect the environment (and others) by limiting the spread of agents.
References for additional information:
Depicted illustration: Safety glasses, safety boots, and safety shoe covers
Picture source & IP:
Safety Eyewear.jpg - Wikimedia Commons
Haix boots.jpg - Wikimedia Commons
Shoes in shoe covers 3.jpg - Wikimedia Commons
Text source & IP:

## Slide 14: What types of PPE are available to you?
What type of PPE do you use, and in what (CBRN) circumstances?
Are you aware of PPE of other first responder units?
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: What types of PPE are available to you?
Result: Students learn about some additional PPE from other units.
Instructions for the teacher: Explain that it is necessary not only to be able to choose appropriate PPE for yourself, but also if other units have appropriate PPE available.
It is possible that other first responder units, that you have to cooperate with, do not have the appropriate PPE available. Or the other way around, that you cannot assist due to lack of PPE.
You can ask your students when if they think it is appropriate to share (surplus) PPE
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 15: Take home message
PPE is essential at a CBRN incident scene and is chosen based on
  Symptoms of victims
  Environmental indicators
PPE is selected based on the protection of specific parts of the body
  Respiratory tract: Breathing apparatus, respirators and face masks
  Skin: coveralls, gloves, boots, glasses
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Take home message
Result: The students are made aware of the various types of PPE.
Instructions for the teacher:
The take home message is that PPE is essential at a CBRN incident scene.
In addition, choosing the right type of PPE is very important. However, when in doubt increase the level of protection.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 16
Thank you for your attention
Melody Presentation 5.4. Personal protective Equipment (PPE)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Topic: 5.4 Personal Protective Equipment (PPE)
Melody Presentation 5.4. Personal protective Equipment (PPE)
Learning objective: To recognize some different types of PPE and recognize how to carry out some basic techniques
Title slide: Thank you for your attention
Result: Students and teacher wrap up this part of the curriculum and can enter the next topic.
Instructions for the teacher: Time for questions or remarks.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: