## Slide 1: Module 5 Risk assessment on scene and hazard avoidance
5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Module 5 Risk assessment on scene and hazard avoidance
Result: trainee are made aware of the contents of this MELODY module
Instructions for the trainer: Note that in this MELODY module various types Treatment methods of patients will be explained.
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To recall some different DIM techniques (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: learning objective
Result:
Instructions for the trainer:
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: DIM
What does DIM mean?
3
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: DIM introduction slide
Result: trainees are asked if they know what the term DIM means and discuss the possible differences between the three definitions
Instructions for the trainer:
Ask the trainees if they know what DIM means.
You can lead the discussion for about a minute and then ‘show the answer’
DIM = Detection, Identification, Monitoring
Maybe differences have been mentioned already. The next slide will go into detail considering the differences.
References for additional information:
Depicted illustrations:
A chemical glove holding a detection device for Chemical Warfare Agents and Toxic Industrial Compounds.
Picture source & IP: https://commons.wikimedia.org/wiki/File:An_instructor_at_the_Defence_NBC_Centre_operates_the_Manportable_Chemical_Agent_Detector_MOD_45148143.jpg
Text source & IP:

## Slide 4: DIM
Detection
The act of locating CBRN hazards or discovering or perceiving the presence of CBRN agents.
Identification
The clear and qualitative determination of which CBRN substance / material is present.
Monitoring
A continuous or periodic process of qualitatively or quantitatively determining the presence or absence of CBRN substances.
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: DIM
Result: trainees have a basic idea that techniques are available to detect the presence of CBRN agents
Instructions for the trainer:
DIM = Detection, Identification, Monitoring
Detection
The definition as is given in the EU CBRN Glossary:
The act of locating CBRN hazards or discovering or perceiving the presence of chemical, biological, radiological, nuclear agents.
In a practical sense these techniques:
Are usually relatively easy to apply
Can give instant results in the field
Have a high uncertainty regarding sensitivity and specificity (false positive results and false negative results)
Usually need high concentrations of the CBRN agent to be successful
Usually used to detect ‘danger’
An example most of the trainees will know is pH-paper, which can be used for the detection of acids or bases
Another example would be the “Geigerteller”, a monitor used to detect radiation. A dose-response device for personal protection would be another device in this category.
Identification
The definition as is given in the EU CBRN Glossary:
The clear and qualitative determination of which CBRN substance / material is present.
In a practical sense these techniques:
Are to be deployed by well trained specialists
Are not always available in the field (e.g. often samples are taken and analyzed in a laboratory)
Are used to identify a CBRN substance, much like fingerprinting is used to identify a suspect.
Most trainees will know that specialized tests are done in dedicated laboratories
Monitoring
The definition as is given in the EU CBRN Glossary:
A continuous or periodic process of qualitatively or quantitatively determining the presence or absence of CBRN substances.
In a practical sense these techniques:
Can be both techniques used for detection or identification.
The term monitoring refers to the fact that these techniques are used over a longer period of time and ensures a constant measurement of presence.
An CBRN Chemical (warfare) example for the need of monitoring would be the following:
  A surface is contaminated with VX
  It is known that VX will slowly evaporate until none is left, however this process can take weeks.
  To know when all VX is gone you could measure for weeks, until none is detected or identified.
A CBRN Chemical or Biological example for the need of monitoring would be the following:
  Drinking water is continuous monitored for substances that should not be in it
  This includes all kind of chemicals (for instance pesticides, metals, etc.) AND biological parameters (for instance E. coli bacteria, etc.). Monitoring biological parameters (and some chemicals) require a laboratory setting and well-trained specialists
  Radiological monitoring of drinking water is done as well
An CBRN Radiological example for the need of monitoring would be the following:
  A company collecting and selling scrap metals wants to assure no radioactive metals enter the company
  Therefore, detection gates are installed.
  All trucks entering the company are ‘monitored’ for radiation with detection equipment
Some techniques might be made available to the trainee. Remember that no matter how simple a technique is, practical training will be necessary.
Discuss techniques trainees know and that are available to them.
Most techniques will be applied by specialists. It is important to know how to escalate to that specialist level if you feel this is necessary.
References for additional information: -
Depicted illustrations:
Left - Military detection paper for chemical warfare agents
Middle – laboratory
Right - Explosion/oxygen detection equipment
Picture source & IP:
Left: https://commons.wikimedia.org/wiki/File:An_instructor_at_the_Defence_NBC_Centre_operates_the_Manportable_Chemical_Agent_Detector_MOD_45148143.jpg
Middle: https://nl.wikipedia.org/wiki/Laboratorium#/media/Bestand:Laboratorium.jpg Creative Commons Attribution-Share Alike 3.0 Unported
Right: RIVM
Text source & IP:

## Slide 5: Chemical detection and identification
Detection
Detection paper for chemical warfare agents
Paper submerged in liquid, colouration indicates mustard gas, volatile nerve agent or nonvolatile nerve agent
Identification
Gas chromatography mass spectrometer
Equipment can identify millions of chemical substances and the amount
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Chemical detection and identification
Result: The trainees understand the differences between detection and identification
Instructions for the trainer: explain that this slide provides two examples of detection and identification technologies, of which pH paper is a very simple one (left photo), and gas chromatography a more specialized one (right photo)
References for additional information:
Depicted illustration: Left: Detection papers to detect CWA, Right: Gas Chromotography mass spectrometer
Picture source & IP:
Left: https://www.bvv.cz/idet/aktuality/oritest-spol-s-ro/
The Melody consortium has done its utmost to trace the copyright owner of the photo used in the current presentation under fair use conditions. In case your photo hasn’t been properly acknowledged, please contact www.melodytraining.eu and the photo will be removed.
Right: https://commons.wikimedia.org/wiki/File:GCMS_closed.jpg,
Creative Commons Attribution-Share Alike 4.0 International, 3.0 Unported.
Text source & IP:

## Slide 6: Some examples of chemical detection equipment
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Some examples of chemical detection devices
Result: The trainees will be aware that many different devices are available for chemical detection.
Instructions for the trainer:
Explain there are all kinds of devices on the market with different pro’s and con’s
Most of them are meant to detect a certain group of chemical substances, this means most of the time you need to have some idea of what you are looking for
This kind of detection equipment is usually deployed by the fire department and the army
If you have some knowledge about these techniques, you might want to explain in some more detail.
References for additional information:
Depicted illustration:
Left two pictures are devices that use light (infrared or raman) to identify substances using a library of known substances
The middle two pictures are gas detection tubes to identify and quantify substances if you know what to look for (e.g. you would have a specific tube for chlorine)
The right two devices, use ion mobility spectrometry to identify substances. This kind of devices typically have different modes, for instance a Chemical Warfare Agent modus or a Toxic Industrial Chemicals mode.
Picture source & IP:
Brochures sales companies.
The Melody consortium has done its utmost to trace the copyright owner of the photo used in the current presentation under fair use conditions. In case your photo hasn’t been properly acknowledged, please contact www.melodytraining.eu and the photo will be removed.
Text source & IP:

## Slide 7: Biological detection and identification
Detection
Proteins: Immunoassays
DNA: Polymerase chain reaction (PCR)
Identification
Mass-spectrometry based on proteins
Rapid DNA sequencing based on DNA
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Biological detection and identification
Result: trainees have learnt that for biological agents handheld simple detection equipment exists. These are usually based on detection of specific proteins of DNA from pathogens. Methods vary in their level of sensitivity and specificity and in general for improved performance the required equipment gets more complicated (and bigger).
Instructions for the trainer:
Explain that specific detection is mostly based on the detection of proteins or DNA sequences.
The most rapid and simple detection systems are based on immunoassays (similar to pregnancy tests), but these are the least sensitive and specific, so may miss an agent or produce false positive results. The example kit detects multiple pathogens (in addition to toxins) within minutes
Very sensitive and highly specific results can be obtained when detecting specific DNA sequences. The detection methods are more complicated, but many systems have been and are being developed to make these methods faster and user-friendly. The example presents a method for the detection of an array of 16 bacteria, viruses and toxins within an hour on a ‘sample in – result out’ basis.
Detailed identification of biological agents to yield detailed information (e.g. virulence) can be done by using MALDI-TOF mass spectrometry or DNA sequencing. These methods can be rapid (MALDI in the order of minutes, sequencing hours), but requires highly trained specialists. In addition, identification by MALDI-TOF requires isolates of bacterial strains, which limits application in the field. Similar to the above, there are developments to make these techniques more accessible and user-friendly, but field-employment is not likely.
References for additional information:
Depicted illustration: A RAID Immunoassays for detecting Proteins, A PCR for detecting DNA (a filmarray), A Bruker Biotyper Mass-spectrometry for identification based on proteins, A minion, Rapid DNA sequencing for identification based on DNA
Picture source & IP:
Brochures sales companies.
The Melody consortium has done its utmost to trace the copyright owner of the photo used in the current presentation under fair use conditions. In case your photo hasn’t been properly acknowledged, please contact www.melodytraining.eu and the photo will be removed.
Text source & IP:

## Slide 8: Radiological detection and identification
Detection
α-radiation usually not possible
β-radiation difficult
γ-radiation usually easy (dosimeters or Geiger tubes)
Identification
RN material can be identified
  through γ radiation, advanced training required
  through α only by experts with advanced equipment
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Radiological detection and identification
Result: trainees know that handheld devices can distinguish between α, β and γ radiation. γ is easy to detect with simple and cheap equipment. Identification of the RN material is possible in the field when it emits gamma radiation, but α and β is only possible in the lab (by experts).
Instructions for the trainer:
Explain that "detection" and "identification" can have different meanings for RN with respect to the use in the CB-"world", and, also how these terms are used
1) detection and identification: whether it is alpha, beta or gamma radiation
2) detection and identification: meaning the presence of radioactive material and identifying the radioactive isotope that emits the radiation
Handhelds can distinguish between alpha, beta, and gamma radiation.
Detecting α and β radiation can be tricky or even impossible in the field, Especially α radiation due to the very short distance alpha radiation can travel through air: the detector should be a few millimetres from the source for a proper detection. Detection of alpha might be impossible for the simple reason that the object does not have a flat surface, and thus prevents the detector being placed close enough to the object. Gamma radiation, on the other hand, is much easier to measure. Simple and low-cost equipment exists to detect the presence of gamma radiation.
More advanced equipment (such as the IdentiFINDER as shown in the picture or similar devices) can be used to identify the isotope in a field setting
Note that expert judgement is still required, and advanced training is necessary to draw conclusions form the measurements.
If trainees ask, explain that devices to identify the radioactive isotope usually measure a gamma spectrum using a low-resolution NaI scintillation detector coupled to a library of commonly encountered radionuclides. If the encountered radioactive isotope happens do be part of the library, then the identification is quite reliable. Vice versa, or in the case of several radioactive isotopes at the same spot, it is not directly clear what the result might be. The instrument gives a false identification with an erroneous reading for the activity or yields a "non-identification".
Experts can take samples like wipe tests and analyse these in the lab using high resolution gamma spectroscopy or Liquid Scintillation Counting that uses the alpha radiation for identification.
A pure alpha or beta source can be easily missed, while a gamma source is much easier.
Detection of gamma radiation does not necessarily indicate a health risks.
References for additional information:
Depicted illustration: Handhelds for radiation detection and identification
Picture source & IP: RIIVM
Text source & IP:

## Slide 9: Take home message
!
Detection methods
  Easy to use in the field, rapid indication. Usually, low confidence
Identification methods
  Requires training, time consuming, often requires a laboratory. Accurate and reliable results
Detection (and identification) not always reliable:
  false positive: agent detected while absent
  false negative: agent not detected while present
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Take home message
Result: The trainees will have some idea of the difference between detection and identification. The trainee understands false results are possible.
Instructions for the trainer: Give the trainees a take home message.
Note:
There are a lot of different techniques, used by fire department, military personnel, sometimes policeman, etc.
Detection methods can be used on site, these techniques usually give a direct result, however with a lower confidence level than lab settings
To positively identify a substance laboratory research is usually necessary. However, even a laboratory setting does not guarantee positive identification of all substances (millions of chemical substances are known, most identification techniques are used for a fraction of those chemicals). Also, identification in the laboratory might take a long time, even weeks.
Remark: symptoms of victims might help to identify a CBRN substance or choose proper identification techniques.
All techniques require some training to properly use them, often a specialist is needed.
Discuss with the trainees the differences and consequence of false positive and false negative results
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 10
Thank you for your attention
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Notes: Module: 5 Risk assessment on scene and hazard avoidance
Learning objective: To recall some different DIM techniques
Melody Presentation: 5.3 Detection, Identification and Monitoring (DIM)
Target audience: Dispatch Officer, Fire Brigade, Police, Ambulance Services, Emergency Medical Services
Title slide: Thank you for your attention
Result:
Instructions for the trainer:
References for additional information: -
Depicted illustration:
Picture source & IP:
Text source & IP: