## Slide 1: Module 6 Task specific response
6.2 Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Module 6 Task specific response
Result:
Instructions for the trainer: No instructions
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 2: Learning objective
To identify possible CBRN threats and to mitigate the effects
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: learning objective
Result:
Instructions for the trainer: No instructions
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 3: - Information gathering, assessment and dissemination - Scene management (zoning, control of CBRN release) - Saving and protecting lives (movement & decon of victims)
Aspects of on scene mitigation
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Aspects of on scene mitigation
Result: After this slide, the trainees have an idea of the main three aspects of mitigating a CBRN incident.
Instructions for the trainer: The initial risk assessment of the situation is not necessarily performed by the Fire & Rescue Services, but should be performed by those First Responders, who arrive first at the scene of the incident. Since these three categories have close similarities to handling non-CBRN incidents, asks the trainees if they can name a few tasks and responsibilities at a CBRN scene.
References for additional information: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014)
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 167

## Slide 4: Information gathering, assessment & dissemination
Establish an overview of the affected area
Estimate the number of casualties/victims
Recognise the signs and indicators of CBRN release
Estimate resource requirements
Provide and obtain regular updates to and from other first responders on scene
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Information gathering, assessment & dissemination
Result: After this slide the trainees have an idea what type of information needs to be gathered, assessed and disseminated.
Instructions for the trainer:
This is a summary of the most important aspects of information gathering, and its assessment and dissemination, for this curriculum. The aspects highlighted within the red rectangle are aspects related to CBRN incidents in particular, and are the focus in the next slides.
The aspects not highlighted are performed by first responders in non-CBRN incidents as well.
Note: the METHANE protocol can be used additionally here as well. The METHANE protocol is explained in Modules 2.4.1 and 4.1.
References for additional information: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014)
Depicted illustration:
Picture source & IP:
Text source & IP: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014), page 5 and 6.

## Slide 5: Recognize the signs and indicators of CBRN release
A visual inspection at the incident scene can give an indication of the physical state of agent(s) released
The physical state of an agent (or upon release), can be:
  Gaseous
  Aerosol
  Liquid
  Solid
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Recognize the signs and indicators of CBRN release
Result: trainees will have an understanding of the physical properties of CBRN agents, in which they can be released
Instructions for the trainer: Explain that
Dispersion range of an agent strongly depends on its physical state
Aerosols are fine solid particles or liquid droplets floating (in suspension) in air and are:
  Composed of (very) fine solid grains (particulate matter), which may contain hazardous C, B, or R/N materials
  Composed of liquid droplets, which may contain C, B, or R/N materials (dissolved, or not)
Particle size is directly correlated to dispersion rate, large particles will in general travel less far than smaller particles
Weather conditions (wind speed, wind direction, temperature, humidity) severely affect dispersion of matter suspended in air.
Liquids will start evaporation when released. Some liquids will evaporate quickly, others very slowly. For instance (some) CWA agents like Mustard gas or VX will not evaporate quickly under normal weather conditions. Therefore, these types of CWAs can remain hazardous for longer periods of time after the release, than more volatile CWAs.
Solid particles, containing C, B, or R/N materials, can be resuspended in air multiple times and dispersed over larger areas. However, concentration of airborne particles will be reduced over time, especially when the source can be located and removed. The concentration of deposited particles may accumulate locally over time, depending on the weather conditions.
References for additional information: -
Depicted illustration: Matter states and processes
Picture source & IP: Melody
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 167

## Slide 6: Recognize the signs and indicators of CBRN release
Inspection of important properties can be assessed by ADR signs, UN number(s), Hazard signs, or MSDS sheets.
Important properties regarding dispersion:
  Volatile / Flammable / Explosive / Corrosive / … properties
  Toxic / Infectious / Radiological properties
  (non)dissolvability in (non)organic solvents
  Vapour pressure
  Vapour or gas heavier or lighter than air?
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Recognise the signs and indicators of CBRN release
Result: trainees will have an understanding of a number of important additional properties of CBRN agents, in which they can be released
Instructions for the trainer: Note to the trainees that this list of additional properties of CBRN agents is not complete.
These properties may provide the trainees with important clues regarding the type of incident and/or type of agents released.
For instance, when the UN number, ADR or hazard signs, or in absence of these, a visual inspection indicates the release of corrosive materials, a release of a biological agents is highly unlikely.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 167

## Slide 7: Estimate resource requirements
Consider deploying additional first responders or specialists
  First responders with proper PPE (respiratory & dermal)
  Detection, Identification & Monitoring teams (DIM)
  Medical facilities (ambulances, EHS, (field) hospitals)
  EOD units
  Decontamination units (infrastructure, vehicles, people, pets)
  Law enforcement
  Forensic specialists
  …
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Estimate resource requirements
Result: The trainees learn about the resource requirements for the scene of a CBRN release
Instructions for the trainer: An important aspect is to be able to assess if additional assistance is required, both from additional first responders or specialists.
State that proper PPE is also a resource requirement, and when lacking, the actions of first responders arriving on a CBRN scene are severely limited.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014).

## Slide 8: Scene management (zoning, control CBRN release)
Establish inner & outer cordon (hot/warm/cold zone)
Established multi-agency command point (cold zone)
Contain contaminant release
Consider utility shutdown
Cordon off contaminated areas, or shielding
Establish a holding area for contaminated victims
Establish decontamination and triage areas
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Scene management (zoning, control CBRN release)
Result: After this slide the trainees have an idea what type of information needs to be gathered, assessed and disseminated.
Instructions for the trainer:
The aspects mentioned here are still very general. Details depend on the type of CBRN incident.
This is a summary of the most important aspects of scene management for this curriculum.
The aspects highlighted within the red rectangle are aspects related to CBRN incidents in particular, and are the focus in the next slides.
Aspects not highlighted are performed by first responders in non-CBRN incidents as well.
References for additional information: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014)
Depicted illustration:
Picture source & IP:
Text source & IP: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014), page 5 and 6.

## Slide 9: Contain release and eliminate contaminant
Containment:
  Limit dispersion & evaporation
  Consider utility shutdown
Source elimination:
  Removal of agents or dilute concentration
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Contain release and eliminate contaminant
Result: The trainees will learn about a number of mitigation options that can be deployed in case of an CBRN incident.
Instructions for the trainer: Explain that elimination of the source (if still present) is the most important objective of response.
However, source elimination is often not the particular task of a First Responder. Elimination should be done by experts or secondary responders.
First Responders, when adequately equipped with PPE, can be (made) responsible for containing released solids and liquids, if possible. Mitigation of further release may also be achieved by utility shutdown or other means, such as: closing sewer(s valves), setting up improvising barriers (e.g. vehicles or road blocks) or dams (e.g. sand bags) to avoid further dispersion.
Shielding (e.g. from radiation exposure) can also be improvised by positioning of vehicles or shelter in place in buildings. Fire brigades can also use water to dilute CBRN agents, although often resulting in contaminating larger areas, or use water screens as a protective barrier to prevent dispersion of airborne agents.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 167

## Slide 10: Containment and elimination of liquids
Containment:
  Limit dispersion by closing valves or building dams
  Limit evaporation by covering liquids with foam
Elimination:
  Use absorbent materials to remove liquids
  Dilute liquid agents to reduce concentration
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Containment and elimination of liquids
Result: The trainees will learn about a number of mitigation options for liquids that can be deployed in case of an CBRN incident
Instructions for the trainer: Bags filled with sand or building a basin can be used as a dam to contain the liquid and preventing it spreading further. It will keep the contaminated area as small as possible.
Spraying foam on a puddle of liquid will minimize the evaporation. It is important is to maintain the layer of foam by spraying foam if needed.
Absorbent materials can be used to stop evaporation of the liquid and can be used to remove or clean up the liquid. The used materials should be put in big barrels afterwards.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 170

## Slide 11: Containment of gaseous vapour or clouds
Containment:
  Gas or vapour clouds are hard to contain
  Limit dispersion using water screens (if possible)
Elimination:
  Use absorbent materials to remove volatile liquids
  Gas or vapour clouds will dilute when airborne
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Containment of gaseous vapour or clouds
Result: The trainees will learn about a number of mitigation options for gaseous or vapour clouds that can be deployed in case of a CBRN incident
Instructions for the trainer: Before you show this slide, discuss with trainees what mitigation methods they have and/or would use when there are gaseous vapours or clouds involved.
A gas cloud or vapour can quickly form during an attack with Chemical War Agents (CWAs). Gaseous agents will be released directly as gas. Non-persistent CWAs will quickly form a vapour, because even though they are dispersed as liquid, their volatility means that they will evaporate quickly. Only very persistent CWAs will remain in liquid phase for a long time.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 170

## Slide 12: Containment and elimination of solids
Containment:
  Limit dispersion by covering (e.g. plastic sheets).
  Limit dispersion by covering with foam (powders)
Elimination:
  Use inert containers to remove solids.
  Dilute with liquids to reduce concentration
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Containment and elimination of solids
Result: The trainees will learn about a number of mitigation options for solids that can be deployed in case of n CBRN incident
Instructions for the trainer: Before you show this slide, discuss with trainees what mitigation methods they have and/or would use when there are solids involved.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 169

## Slide 13: Cordon off contaminated areas or Shielding
Shielding from exposure:
  Limit exposure by strategic positioning of vehicles, road-blocks
    Limit access to contaminated area
    Limit exposure to radiation
  Limit exposure by sheltering in (not contaminated) buildings
    Limit exposure to C, B and R agents
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Cordon off contaminated areas or Shielding
Result: The trainees will learn about a number of mitigation options for shielding that can be deployed or used in case of a CBRN incident.
Instructions for the trainer: If source elimination and/or containment possibilities are very limited or not possible, shielding is one of the options available as well. Mitigation may already be obtained by setting up improvising barriers (e.g. vehicles or road blocks) to limit further exposure. Shielding (e.g. from radiation exposure) can also be improvised by positioning of vehicles or shelter in place in buildings.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: NIBRA 2005; Handbook NBC (2e printing); paragraph 4.1.2 – page 169

## Slide 14: Saving and protecting life
Provide safe systems of work for rescuers
Carry out necessary rescues
Implement medical triage and treatment
Implement decontamination as appropriate
Consider requirements and provide transport for victims
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Saving and protecting life
Result: After this slide the trainees have an idea what actions are needed to save and protect lives.
Instructions for the trainer:
The aspects mentioned here are again still very general. Details depend on the scale and type of CBRN incident.
This is a summary of the most important aspects of saving and protecting lives, for this curriculum.
The aspects highlighted within the red rectangle are aspects related to CBRN incidents in particular, and are the focus in the next slides.
Aspects not highlighted are performed by first responders in non-CBRN incidents as well.
References for additional information: Guidelines for first responders to a CBRN incident- NATO Civil Emergency Planning Civil Protection Group (update 2014)
Depicted illustration: First responder giving directions towards decontamination and medical aid facilities
Picture source & IP: Photo by Elfriede Thiessens, linkedin.com/in/elfriede-thiessens-8b3b463a, photo Licensed to Melody
Text source & IP: GUIDELINES FOR FIRST RESPONDERS TO A CBRN INCIDENT - NATO Civil Emergency Planning Civil Protection Group (update 2014), page 5 and 6.

## Slide 15: Implement medical triage and treatment
Depending on type of CBRN incident and state of victims:
  Perform medical triage and treatment
    Based on START (Single Triage and Rapid Treatment) or MASS (Move, Assess, Sort, Send) protocols
  Perform decontamination triage
    Based on prioritization of (a)symptomatic and (non)ambulatory casualties
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Implement medical triage and treatment
Result: trainees know what is meant by medical triage and decontamination triage
Instructions for the trainer: Explain that for some victims decontamination needs to be performed before adequate triage and treatment can occur. Separation of victims for decontamination triage is somewhat different from medical triage and its priorities. What comes first depends on the type of CBRN incident and type of injuries. Details of the triage systems that are mentioned (START and MASS) will be explained in subsequent slides.
Medical triage will most likely be the responsibility of medical staff and might require prior decontamination (by law). It is useful for Fire & Rescue Service personnel to be informed about the triage process, but they should focus on their assisting function such as in decontamination.
References for additional information: - Guidelines for Mass Casualty decontamination during Hazmat/weapons of Mass destruction incident: volumes I and II. U.S. Army Edgewood Chemical Biological Center, Aberdeen Proving Ground, MD. August 2013.
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 16
Triage Categories:
=
=
=
1. Immediate (red)
X
=
Patients requiring emergency life-saving treatment
2. Delayed (yellow)
3. Minimal (green)
4. Dead/expectant (black)
Delay in medical treatment permitted, patient generally not able to walk
Relatively minor signs and symptoms, patient is able to walk independently
Patient lacks vital life signs and unresponsive to stimuli
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Triage categories
Result: trainees learn about the 4 triage categories
Instructions for the trainer: Do the trainees remember the triage categories? Explain in more detail the following:
Triage is the process of determining which victims require medical (life-saving) treatment most urgently.
The groups are in general:
immediate (red) - immediately life threatening problems with a high potential for survival; Patient cannot survive without immediate treatment, Patient with high chance of survival with introduced therapy. Patient is not able to move, require medical assessment
delayed (yellow) – serious injuries, require medical care but management can be delayed without increasing morbidity or mortality; for patients in this category some delay in medical treatment is permitted, although some continuing care and pain relief may be required before definitive care is given.
minimal (green) - require minor care or no care without adverse effect; Can care for themselves, Can be helped by untrained personnel.
Dead/expectant (black) – very serious injuries, patient lacks vital life signs and unresponsive to stimuli. Patient is dead or expectant (life threating with low chance of survive) Expectant should receive comfort care until resources available, Life threatening conditions beyond the treatment capabilities of the available medical personnel.
Explain that the order presented on the slide is also the commonly used order of treatment. Create designated areas on/near the incident scene for the different triage categories.
Each country uses different triage systems. Most systems use the presented colours, numbers and/or category names.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 17: TRIAGE in the field
Two types of triage systems that are discussed
START Triage (Single Triage and Rapid Treatment)
  System based on individual physiological indicators
  Divide victims based on severity of injuries (ABCDE)
  Quick triage (in +/- 30 seconds)
MASS Triage (Move, Assess, Sort, Send)
  System based on rapid grouping of victims
  Divide victims based on health status
  Verbal commands to separate groups
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Triage in the field
Result: trainees are familiarized with triage systems START and MASS.
Instructions for the trainer:
The aim in executing the START triage is to divide the victims according to the severity of the injuries and potential to survive into 4 groups. The person executing the triage in approx. 30 second needs to categorize the victims on the basis of ABCDE (Airways, Breathing, Circulation, Disabilities, Exposure) protocol. Each victim needs to be tagged with the appropriate color in order to prioritize the medical intervention and evacuation to the point of care.
The aim of the MASS triage is to divide the victims into categories according to the seriousness of injuries or health status. However, in contrast to START system, the MASS triage uses verbal commands at first to allow separation of minimal and delayed groups of victims. Next in this triage system is to identify dead victims, who should be tagged. Then, the rest of the victims belong to the remaining two categories – immediate or expectant.
The detailed explanation of execution of both systems will be provided in next slides.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 18
Triage category | Physiological effects | Treatment order
1. IMMEDIATE | Breathing only after airway is cleared, OR Respiratory rate: <9/min, or, >30/min, OR Capillary refill time >2 sec. | IMMEDIATE TREATMENT
2. DELAYED | Unable to walk, AND, Respiratory rate 10-30/min, AND Capillary fill rate ≤ 2 sec | DELAYED TREATMENT
3. MINIMAL | Wounded but able to walk independently | NO RISK TO LIFE AND HEALTH
4. DEAD/EXPECTANT | Not breathing, even after clearance of airway | NO TREATMENT (decontamination may be needed)
START Triage - Physiological effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: START Triage - Physiological effects
Result: trainees learn that the START disaster triage is based on physiological signs.
Instructions for the trainer: The START Triage (Single Triage and Rapid Treatment) is based on the severity of injuries. The system is based on the following criteria: airway, breathing, circulation, disability, exposure (ABCDE). The person executing the triage procedure has approximately 30 seconds to categorize patients to one of the following categories: immediate, delayed, minimal or expectant/dead. START is using a four-color coded system to mark the victims.
Make sure to wear appropriate PPE when assessing physiological effects of patients.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 19
START Triage
Scheme
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: START Triage scheme
Result: trainees should be familiarized with basic principles of executing the START triage system.
Instructions for the trainer: Present the scheme and emphasize that, the patients’ capability to breathe and his/her breathing frequency largely determines the urgency in medical care. This scheme can be used to quickly assess the triage category a patient should be assigned to.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 20: START Triage Tag
Mettag
AVPU – alert, verbal, painful, unresponsive
BP – blood pressure
RESP – respiratory rate.
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Triage card
Result: trainees should be familiarized with the example of triage card as a part of triage protocol.
Instructions for the trainer: A triage tag is a tool used by first responders and medical personnel during a mass casualty incident. With the aid of the triage tags, the first-arriving personnel are able to effectively and efficiently assign limited resources and provide necessary immediate care for the victims. Triage tags are placed near the head. Triage tag should also be used to record any treatment given. Although expectant and dead are seen as one category in the START triage system, there are separate labels on the triage tag.
Nowadays, in order to avoid under or over triage (improper triage categorization), electronic devices are used. The devices will prevent the influence of human factors on executing procedure
Abbreviations used: APVU: Alert, responds to Vocal stimuli, responds to Painful stimuli or Unresponsive to all stimuli , BP – blood pressure, RESP – respiratory rate.
References for additional information: -
Depicted illustration: Triage tool
Picture source & IP: https://tacda.org/product/mt-501-salt-method-mettag-triage-tag/
The American Civil Defense Association, purchased by SCK-CEN. Permission to use received.
Text source & IP:

## Slide 21: MASS Triage System
M ove the patients into groups – patients with ability or lack of ability to walk
A ssess the patients' clinical condition individually – assign triage categories
S ort the patients to victims collection points
S end the patients to hospitals or other medical treatment facilities
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS CBRN Triage System.
Result: trainees should be familiarized with MASS triage system.
Instructions for the trainer: The MASS system is used to prioritize medical assistance and evacuation.
M stands for Moving patients into groups, allowing recognition of patients with and without the ability to walk.
A stands for medical Assessment.
S stands for Sorting patients to dedicated triage category points.
S stands for Sending victims to dedicated places (hospital, point of care), where medical assistance will be provided.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 22: MASS – Step by step action
Step 1
    Goal: to separate the ambulatory patients
Action:
  Verbal instructions: ” Everyone who needs medical attention, should walk to the area marked by the green color ”.
  Result: Patients with ability to walk will walk to the designated area
Result:
  Minimal Group of patients
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action Result: trainees should know how to perform step 1 in the MASS triage system: separation of minimal group of patients.
Instructions for the trainer: The first step in executing the MASS triage is to recognize the patients with and without the ability to walk. Ask the trainees which action they would take to achieve this goal, then present the rest of the slide.
The first step in MASS triage, is to separate the minimal group of victims. In order to execute this task, a loud verbal instruction must be given: “Everyone, who needs medical attention, should walk to the area marked by the green color”. In most cases, patients from the minimal category will move to the designated area. The remaining groups on the scene are immediate, delayed or expectant/dead.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 23: MASS – Step by step action
Step 2
    Goal: to separate the patients, which do not need immediate medical attention
Action:
  Verbal instruction: ” Everyone who needs medical attention, should wave using an arm or a leg so we can find you ”
  Result: patients with ability to move their arms or legs will obey
Result:
  Delayed Group of patients
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action Result: trainees should know how to perform step 2 in the MASS triage system: separation of delayed group of patients.
Instructions for the trainer: The second step in MASS triage system is to separate the delayed group of victims. Ask the trainees which action they would take to reach the goal, then present the rest of the slide.
Similar to step one, step two is also based on verbal command. “Everyone who needs medical attention, should wave their arm or leg so we can find you”. As a result, the delayed group of patients will be recognized. These patients are not able to walk but their mental status allowed them to understand the verbal command and respond by moving their arm or leg. In most of the cases, their medical condition is not life threating, so they should be categorized as ‘delayed’ group of patients. The remaining victims on the scene now belong to the categories ‘ immediate’ and ‘ expectant/dead’ .
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 24: MASS – Step by step action
Step 3
    Patients not moving categorized as:
      Immediate (red)
      Dead/expectant (tag)
Patients not able to walk but able to move belong to the Delayed Group
Patients able to walk belong to the Minimal Group
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action Result: trainees should know that in step 3 of the MASS triage system, patients have been separated into three categories: delayed, minimal and a third group which consist of two triage categories: immediate and expectant/dead.
Instructions for the trainer: Ask the trainees to identify the groups of patients that have been created after performing the previous two steps.
After their input, explain that victims have now been divided into three groups. The minimal group and delayed group were identified and separated. The remaining groups consist of two triage categories: immediate and expectant/dead.
Be aware that vocal communication might not work for everyone, for example due to impaired hearing or language difficulties. Also note that patients might be non-ambulatory due to pre-existing medical conditions.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 25: MASS – Step by step action
Step 4: Medical assessment of patients not moving:
Dead (black)
  Tag dead victims
Differentiate Immediate (red) from expectant (grey)
  Medical assessment required
  Stabilize patients and tag them
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action
Result: trainees should know what step 4 in the MASS triage system entails: Identification of dead victims and of the group of patients who remain at the scene, who may belong to triage categories ‘ immediate’ or ‘ expectant’.
Instructions for the trainer: In step four of the triage, dead victims are identified and separated. Dead victims are tagged in order to prevent re-triage. As a result, the remaining group at the scene consists of immediate and expectant victims. At this point, a rapid medical assessment is required to differentiate immediate from expectant. It should be pointed out that, in contrast to START triage, only at this point medical assessment of the patients is performed. This speeds up the triage process and saves time which ultimately may save lives.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 26: MASS – Step by step action
Step 5: Sort patients
    Count the victims in each triage category
    Move the victims to the areas designated for each triage category
    Report number of victims
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action
Result: trainees should know how to perform step 5 in the MASS triage system: counting and sorting of victims in each triage category and reporting to the crisis manager.
Instructions for the trainer: The next step in MASS triage is to estimate the number of victims in each triage category. The number of the victims and categories should be provided to the crisis manager. If possible, the immediate and expectant groups should be separated, and designated areas should be clearly marked. This will speed up the process of medical evacuation.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 27: MASS – Step by step action
Step 6: Treatment and evacuation of patients according to triage categories
      Immediate →Delayed→ Minimal→ Expectant/Dead
  Alternative transportation (buses, minivans) for minimal patients
  Alternative medical treatment facilities for minimal patients
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action
Result: trainees should know how to perform step 6 in the MASS triage system: medical treatment and evacuation priorities in the MASS triage system.
Instructions for the trainer: The subsequent step in MASS triage is to execute medical treatment and evacuation. The priority in medical treatment and evacuation is as follows: Immediate →Delayed→ Minimal→ Expectant/Dead. It should be mentioned, that in case of a mass casualty event that exceeds routine transportation capabilities, alternatives transportation may be used. E.g., minibuses or vans can be used for the minimal group.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 28: MASS – Step by step action
Step 7
  At the point of care, perform reassessment (re-triage) to confirm the Immediate and Expectant triage categories and to provide necessary medical assistance.
On the scene, manage dead victims
  Potential source of secondary contamination or infection
  Do not move bodies (exception – providing access to living patients)
  Avoid destruction of evidence
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action
Result: trainees should know how to perform step 7 in the MASS triage system: re-triage and on the scene post evacuation activities.
Instructions for the trainer: The final step in MASS triage is to re-triage the victims at the point of care (dedicated hospitals). Emphasized that re-triage is crucial because categories may change during medical evacuation. This step also applies for START triage.
At the scene of the incident, dead bodies must be managed properly after medical evacuation is completed. In CBRN events, dead bodies could be sources of secondary contamination and infection, so they should be properly managed while wearing appropriate PPE. This management of dead victims should be performed by sanitary services according to their procedures.
All activities should be performed in such a way that possible evidence is preserved to enable criminal investigation.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 29: Summary MASS – Step by step action
Verbal instruction: Walk to area  Minimal Group
Verbal instruction: Wave an arm or a leg  Delayed Group
Tag the Dead victims
Perform medical assessment to differentiate Immediate from expectant
Move victims to the designated areas and count the number of victims in each category. Report this.
Medical treatment and evacuation. Priority: Immediate →Delayed→ Minimal→ Expectant
Reassessment (re-triage)
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: MASS – Step by step action Result: trainees should know how to perform step 1 in the MASS triage system: separation of minimal group of patients.
Instructions for the trainer: Summarize the steps in MASS triage as explained in previous slides
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 30: Implement medical triage and treatment
Not all victims require decontamination
Ambulatory, symptomatic
  Can follow simple directions
  Easiest to decontaminate
Non-ambulatory victims
Ambulatory, non-symptomatic
  Have been exposed to the contaminant
Highest priority
Lowest priority
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Implement medical triage and treatment
Result: trainees know how to separate victims for decontamination triage
Instructions for the trainer: Explain that for some victims decontamination needs to be performed before adequate triage and treatment can occur. Separation of victims for decontamination triage is somewhat different from medical triage and its priorities. See also module 6.3 for medical triage and treatment. Presentation 5.7 contains more information about decontamination.
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 31: Take Home Message
Mitigation efforts are divided into three main aspects
Information gathering, assessment and dissemination
  Mitigation efforts should be carried out using proper PPE
  Estimate resource requirements for mitigation purposes
Scene management (zoning, control CBRN release)
  Recognise the signs and indicators of a CBRN release
  Containment of release & elimination of the source
  Shielding from contaminant & cordon off areas
Saving and protecting life
  Implement appropriate medical triage/treatment & decontamination triage
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Take Home Message
Result: trainees are able to summarize the steps often performed to mitigate the effects of a CBRN incident
Instructions for the trainer: This is a summarizing slide and can be used as a bridge to the module 6.3
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP:

## Slide 32
Thank you for your attention
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Notes: Module: 6 Task specific response
Learning objective: To identify possible CBRN threats and to mitigate the effects
Melody Presentation: 6.2: Mitigation methods to limit dispersion, including decontamination
Target audience: Fire Brigade
Title slide: Thank you for your attention
Result:
Instructions for the trainer:
References for additional information:
Depicted illustration:
Picture source & IP:
Text source & IP: